## Slide 1: Data treatment and measurement statistics for time-of-flight neutron scattering experiments
Andrei Savici
Neutron Data Analysis and Visualization Division

## Slide 2: Outline
Motivation
Classical single crystal diffraction data reduction
Revisit the theory for neutron diffraction
Covering reciprocal space – how to improve speed and memory usage for algorithms
Extending the formalism for neutron spectroscopy
More on measurement statistics

## Slide 3: Motivation
What we measure is important, but we can make sense of it only if we know HOW we measure it
By knowing HOW we measure things we can:
  Calculate the statistical significance of the measurements
  Design algorithms and procedures to reduce, visualize, and analyze neutron scattering data

## Slide 4: Motivation
Diffuse elastic scattering
  Neutrons ideal to look at lighter ions
  Limited coverage – need to use multiple orientations
  BUT: no procedure to look at TOF diffuse scattering neutron diffraction data
Diffuse X-ray scattering from b-NaLaF4
A. Aebischer et al., Angew. Chem. Int. Ed. 45, 2802 –2806 (2006)

## Slide 5: Motivation
Inelastic neutron scattering can be used to study magnetic scattering
We want to look at large volumes in the reciprocal space, so we use multiple sample orientations
Current data reduction processes are slow, and use a lot of memory
Magnetic scattering in YFeO3
S. E. Hahn et al., Phys. Rev. B 89 (2014) 014420

## Slide 6: Definitions
Workspace (matrix workspace) – collection of data organized by spectra, containing either a histogram or a list of events
MD Workspace (multi dimensional) – MD events or MD boxes (MD bins) have multiple coordinates
NOTE: an MD event is not necessarily a neutron event
z is along the beam,
y vertically up,
x in the horizontal plane

## Slide 7: What do we measure?
Neutron events – TOF and detector position (maybe wall clock time). Some store these as histograms
What we want is the differential scattering cross section

## Slide 8: Single crystal diffraction data reduction
ConvertToMD – with Lorentz correction
FindPeaksMD
FindUB
IndexPeaks
IntegratePeaksMD
SavePeaks – but doing Anvred and spectrum corrections

## Slide 9: What is Lorentz/spectrum correction?

## Slide 10: Diffuse scattering – raw data

## Slide 11: Adding normalized data

## Slide 12: Lessons learned from TAS
When adding data together we add monitors together and plot summed data divided by monitor data
This accounts for different integrated flux on the sample
The important quantity is not the neutron count, but the normalized neutron count
Order of operations is important

## Slide 13: Neutron diffraction - the correct way
Need to find out the correct normalization
is not an additive quantity
Correct way to write the above equation is

## Slide 14: Using incoherent scattering (vanadium)
For incoherent scattering, the differential cross section is a constant
With the exception of an overall factor (the total incident flux), if one measures incoherent scattering only, in the same conditions as the sample, one finds

## Slide 15: Example
[H,K,-2.5] [H,K,-3] [H,K,-3.5]
[H,K,-4] [H,K,-4.5] [H,K,-5]

## Slide 16: Lorentz and spectrum corrections (II)
Approximation of small volume
Has the same wavelength and angular dependence as the Bragg peaks
C is a constant that does not depend on wavelength, flux, detector

## Slide 17: Procedure outline
Treat data as before, but no proton charge normalization, and without Lorentz/spectrum corrections
For each orientation/measurement create an equivalent incoherent scattering dataset
  Copy the goniometer settings
  Copy the UB
  Multiply with data proton charge
  Convert to MD
Bin all real data and incoherent normalization data on the same MD grid
Sum data, sum normalization, then divide

## Slide 18: Memory and statistics problems
Keeping vanadium in events is very memory intensive (24GB per rotation)
Solution: switch to 3D histogram early (3GB – independent of number of rotations)
Low number of detectors contributing to each HKL box means low statistics
Solution: average all detector pixels in a bank (feasible only on histogram data)
Slow (3-4 hours to change the bin size for the whole dataset)
Solution: do something new

## Slide 19: Next generation diffraction normalization
For TOF diffraction, the biggest problem is calculating the incident neutron flux that contribute to each MD box
For each detector trajectory in reciprocal space calculate the intersection with each MD box
Integrate vanadium scattering (proportional to incident, momentum dependent flux) between the momenta corresponding to those intersections

## Slide 20: How to calculate intersections?
Apply to minimum and maximum wavevectors
What if ?

## Slide 21: How to integrate flux?
We need to calculate the integrated flux between two wave vectors for every detector that has a trajectory passing through a particular MD box.
For better statistics, we can group detectors that have the same energy response.
To improve speed and memory – calculate the indefinite integral. The integral in the MD box is the difference between the values of the indefinite integral at the two intersections

## Slide 22: Mantid implementation
MDNormSCD
  Input MDEvent workspace
  Binning along different axes
  A workspace containing flux
  A workspace containing solid angle/efficiency
  Output workspace contains data
  Output normalization workspace is the statistical weight
Add output data, add normalizations, then divide

## Slide 23: Mantid implementation
How to create the flux and solid angle workspace?
  Start from raw vanadium, convert to momentum, and crop all spectra to the same values (crop them to the same limits as the data)
  If you bin with a single large step between you obtain the solid angle workspace
  Group together all detectors that have the same energy response (by bank on TOPAZ, all instrument on CORELLI)
  Apply the IntegrateFlux algorithm to obtain the flux workspace
  Save them for later use

## Slide 24: Mantid implementation
What is the performance of this procedure?
  Speed – 10-20 seconds to calculate normalization for each orientation
  Memory – solid angle and flux workspaces are on the order of 10-20 MB. If your MD event workspace for data fits in half of the memory of your computer, you can probably do it on your laptop
Reuse workspaces – processing vanadium is slow and memory intensive. Do it on analysis.sns.gov or on the instrument computers and save the results. Save the MD event workspaces of the data
If possible use autoreduction scripts to process your data, so all you need to do after that is normalize, add and divide

## Slide 25: Single crystal inelastic data reduction
How does the inelastic people keep track of the normalization?
Currently starting from histogram spectra in energy
For direct geometry

## Slide 26: Problems with the current software
Assume all detectors have the same solid angle
Assume all configurations have the same flux
Relies on energy bins being small
Many (most) of those bins are empty. They are just used to see where measurements were performed (very memory intensive)

## Slide 27: Next generation inelastic normalization
dE is the length of a detector trajectory in a MD box along energy transfer
Trajectory is dependent on both incident and scattered momentum
For direct geometry the incident flux is just a number
For indirect geometry the incident flux calculation is similar to the diffraction case

## Slide 28: Calculating intersections
For direct geometry incident momentum is fixed – trajectories are linear in scattered momentum
For indirect geometry final momentum is fixed

## Slide 29: Use intersections for planning tools
Future planning tools based on CalculateCoverageDGS
Input workspace contains instrument description, Ei, goniometer, and UB matrix
Choose basis (HH0, -HH0, 00L)
Select minimum, maximum, and step
Outputs 1 where trajectories intersect boxes
Add multiple orientations or geometries with OrMD

## Slide 30: Mantid implementation
MDNormDirectSC
  Same as before, use DGS reduction
  No proton charge normalization
  See if keeping events yield smaller files
  Calculate normalization for each run
  Add together binned data, binned normalization, then divide
This algorithm is experimental – please provide feedback
Allows for correct accounting of multiple runs, with different proton charge, different geometry, and, with very little work could account for different incident energies (multiply with absolute vanadium factor)

## Slide 31: Future Mantid plans
Integration methods for “normalized data”
Implement indirect geometry normalization
Implement inelastic powder normalization
Implement non axis-aligned bins
Symmetrization
Data processing for reactor based instruments

## Slide 32: What is the errorbar for 0?
The question depends on HOW we measured that 0
For raw data the errorbar is 0
For normalized data the erorbar is 1/normalization

## Slide 33: REMEMBER!
Don’t treat normalized data as if unnormalized:
  Add data together, add normalizations together, and then divide.
  If you need different binning, go back to the original data.
Instrument scientists: be aware of how the measurement is performed.
  Explain the physics to the software scientists, not just give formulas to implement
It is time to revisit many of the approximations and procedures for data analysis

## Slide 34: Acknowledgements
Martyn Gigg, Roman Tolchenov – improve speed
Michael Reuter, Owen Arnold – feedback on the design, nice pictures and movies
Vickie Lynch – help with the initial normalization
Ross Whitfield – testing the new normalization on other datasets
Diffraction data provided by Tara Michels-Clark/ Christina Hoffmann
ORNL and ISIS instrument scientists – feedback
Other group members – feedback
Research conducted at ORNL's Spallation Neutron Source was sponsored by the Scientific User Facilities Division, Office of Basic Energy Sciences, US Department of Energy.